RAT (Radar Tools)

Tutorial “Batch processing with RAT” V1.0

 Batch processing with RAT
Blabla

 Scriptable RAT procedures (and their keywords)
Single channel speckle filters:
If multichannel data is provided, all channels are independently filtered. Complex data are automatically transformed to amplitude data.
- speck_lee,boxsize,looks	(Lee speckle filtering)
  boxsize = filtering window size (default 7)
  looks = effective number of looks of the input data (default 1.0)
- speck_frost,boxsize,damp	(Frost speckle filtering)
  boxsize = filtering window size (default 7)
  dam = damping factor (default 1.0)
- speck_gauss,boxsizex,boxsizey	(Gaussian speckle filtering)
  boxsizex = horizontal filtering window size (default 7)
  boxsizey = vertical filtering window size (default 7)
- speck_mean,boxsizex,boxsizey	(Boxcar speckle filtering)
  boxsizex = horizontal filtering window size (default 7)
  boxsizey = vertical filtering window size (default 7)
- speck_sigma,boxsize,sigfac,looks	(Sigma-Lee speckle filtering)
  boxsize = filtering window size (default 7)
  sigfac = number of stddev to filter (default 2.0)
  looks = effective number of looks of the input data (default 1.0)
- speck_gammamap,boxsize,sigfac,looks	(Gamma-MAP speckle filtering)
  boxsize = filtering window size (default 7)
  looks = effective number of looks of the input data (default 1.0)
- speck_kuan,boxsize,sigfac,looks	(Kuan speckle filtering)
  boxsize = filtering window size (default 7)
  looks = effective number of looks of the input data (default 1.0)
- speck_median,boxsize,sigfac,looks	(Median speckle filtering)
  boxsize = filtering window size (default 7)
  looks = effective number of looks of the input data (default 1.0)
Edge detectors:
If multichannel data is provided, all channels are independently filtered. Complex data are automatically transformed to amplitude data.
- edge_roa4,boxsize	(RoA edge detector with 4 directions)
  boxsize = filtering window size (default 3)
- edge_maxgrad,boxsize	(Lee-RoA edge detector)
  boxsize = filtering window size (default 3)
- edge_robsob,roberts,sobel	(Roberts and Sobel edge detector)
  roberts = set for roberts edge detection (default)
  sobel = set for sobel edge detection
- edge_canny,boxsizex,boxsizey	(Canny edge detector)
  boxsizex = horizontal filtering window size (default 11)
  boxsizey = vertical filtering window size (default 11)
Texture analysis:
- text_varcoef,boxsizex,boxsizey	(Coefficient of variation)
  boxsizex = horizontal filtering window size (default 7)
  boxsizey = vertical filtering window size (default 7)
- text_klee,boxsize,looks,method,amplitude	(Texture inhomogeneity)
  boxsize = filtering window size (default 7)
  looks = effective number of looks of the input data (default 1.0)
  method = type of filtering window (default 1 = boxcar)
  amplitude = set keyword for using amplitude damping (gives an edge detector...)
Various:
slant2ground,height,range,psin,psout	(Slant-to-Ground-Range projection)
height = orbit / track height of sensor over ground (default 5000.0)
range = minimum range to first pixel (has to be left) (default 7000.0)
psin = range pixel spacing of input data (default 3.0)
psout = desired range pixel spacing of output (default 3.0)