RAT (Radar Tools)

Tutorial “Batch processing with RAT” V1.0

 Batch processing with RAT
In the usual evolution of software programs, the GUI (graphical user interface) is developed much later than the program core, and is often considered as an add-on, which fits more or less to the developed routines. Not so in RAT. RAT was from the beginning developed with the goals of immediate graphical visualization of the data and easy of use. Therefore, the data processing and analysing tools were developed simultaneously with the visualization tools and were fully integrated into the RAT graphical framework.
In the meantime, RAT developed into an advanced program, providing many possibilities for high-level radar data processing and analysis. Now RAT reached a state where it can be used for operational data processing, containing a long chain of processing steps. (e.g. starting from data import, to transformation to another data representation, corregistration, calibration, range filtering, and flat earth removal, application of speckle filtering, basis transformation, parameter decomposition and classification.)
To speed up the operational use of RAT, the batch processing is implemented. The intentions behind are
1. fast data processing from the shell without graphical output (which can be very time consuming in case of big data sets).
2. writing of IDL batch programs for automatic and fully operational SAR data processing with RAT procedures.
3. shell-only radar data processing, without any mouse.

 Basic Concepts
- Open IDL shell
- Compile RAT
- Start RAT in the batch mode with
  rat, /nw	;; nw for NoWindow
  - As usual with RAT, if a data set with the name “default.rat” can be found in the current directory, RAT opens it automatically.
  - Alternatively, one can provide a file name to open at the start with
    rat, /nw, startfile=”my_data.rat”
- One can open a new data set with
  open_rat, inputfile=”my_data.rat”
- And, similarly, one can save the current working data set with
  save_rat, outputfile=”my_modified_data.rat”
- The current data set can also be exported to an IDL variable, and used further without interaction with RAT:
  export_var, local_variable
- To exit the RAT batch processing, write
  exit_rat
In a similar fashion, one can import data from external file formats, apply various processing functions, and export it again.
It is of importance to provide all the required parameters to the functions. To find out, which parameters these are, please see this documentation, or consult the IDL source codes of the functions.
It is also important to use the keyword “/CALLED” when calling the procedures from the shell.
Note: This mode is still at an experimental stage. Therefore, it is possible that for some untested procedures, some windows will pop up. Also, some functions are not recommened to use in the batch mode, e.g. there is no reason to call a zoom procedure.
Todo: a procedure to show the preview (snapshot) of the current data in a (direct graphics) window.
In the following, two examples of RAT batch scripting are presented:
1) Simple steps to open a PolSAR data, to do speckle filtering, and to decompose into Entropy/Alpha/Anisotropy. The data is then exported to an IDL variable, which can be further examined, even after exiting RAT.

.r rat
rat, /nw, startfile=”some_polsar_data.rat”
speck_polreflee, smm=7, looks=9, /CALLED
decomp_entalpani, /CALLED
export_var, HAA	;; export the data into the given variable “haa”
exit_rat	;; quit rat batch scripting
help,HAA	;; shows the structure of the still existent variable “haa”

2) Advanced automatic processing: A function to construct a MB PolInSAR data set from a given set of PolSAR data files. Steps: remove the flat earth phase, conduct adaptive range spectral filtering, construct a coherency matrix, apply simultaneously a specified presuming, and do speckle filtering with the Refind-Lee filter. The file is finally saved in the rat format.

pro mbpolinsar_data_processing, polsar_files, fe_file, outputfile, smmx=smmx, smmy=smmy, Lee_box=box
rat,/nw
construct_polinsar, /CALLED, FILES=polsar_files
rrat, fe_file, fe
polin_rgflt_adaptive, /CALLED, fe
polin_k2m, /CALLED, SMMX=smmx,SMMY=smmy
polin_c2t
speck_polreflee, /CALLED, SMM=Lee_box, LOOKS=smmx*smmy
save_rat,outputfile=outputfile
exit_rat
end

These two examples should only show the possibilities of batch scripting. Please feel free to create your own scripts.

 Scriptable RAT procedures (and their keywords)
Single channel speckle filters:
If multichannel data is provided, all channels are independently filtered. Complex data are automatically transformed to amplitude data.
- speck_lee,boxsize,looks	(Lee speckle filtering)
  boxsize = filtering window size (default 7)
  looks = effective number of looks of the input data (default 1.0)
- speck_frost,boxsize,damp	(Frost speckle filtering)
  boxsize = filtering window size (default 7)
  dam = damping factor (default 1.0)
- speck_gauss,boxsizex,boxsizey	(Gaussian speckle filtering)
  boxsizex = horizontal filtering window size (default 7)
  boxsizey = vertical filtering window size (default 7)
- speck_mean,boxsizex,boxsizey	(Boxcar speckle filtering)
  boxsizex = horizontal filtering window size (default 7)
  boxsizey = vertical filtering window size (default 7)
- speck_sigma,boxsize,sigfac,looks	(Sigma-Lee speckle filtering)
  boxsize = filtering window size (default 7)
  sigfac = number of stddev to filter (default 2.0)
  looks = effective number of looks of the input data (default 1.0)
- speck_gammamap,boxsize,sigfac,looks	(Gamma-MAP speckle filtering)
  boxsize = filtering window size (default 7)
  looks = effective number of looks of the input data (default 1.0)
- speck_kuan,boxsize,sigfac,looks	(Kuan speckle filtering)
  boxsize = filtering window size (default 7)
  looks = effective number of looks of the input data (default 1.0)
- speck_median,boxsize,sigfac,looks	(Median speckle filtering)
  boxsize = filtering window size (default 7)
  looks = effective number of looks of the input data (default 1.0)
Edge detectors:
If multichannel data is provided, all channels are independently filtered. Complex data are automatically transformed to amplitude data.
- edge_roa4,boxsize	(RoA edge detector with 4 directions)
  boxsize = filtering window size (default 3)
- edge_maxgrad,boxsize	(Lee-RoA edge detector)
  boxsize = filtering window size (default 3)
- edge_robsob,roberts,sobel	(Roberts and Sobel edge detector)
  roberts = set for roberts edge detection (default)
  sobel = set for sobel edge detection
- edge_canny,boxsizex,boxsizey	(Canny edge detector)
  boxsizex = horizontal filtering window size (default 11)
  boxsizey = vertical filtering window size (default 11)
Texture analysis:
- text_varcoef,boxsizex,boxsizey	(Coefficient of variation)
  boxsizex = horizontal filtering window size (default 7)
  boxsizey = vertical filtering window size (default 7)
- text_klee,boxsize,looks,method,amplitude	(Texture inhomogeneity)
  boxsize = filtering window size (default 7)
  looks = effective number of looks of the input data (default 1.0)
  method = type of filtering window (default 1 = boxcar)
  amplitude = set keyword for using amplitude damping (gives an edge detector...)
Various:
slant2ground,height,range,psin,psout	(Slant-to-Ground-Range projection)
height = orbit / track height of sensor over ground (default 5000.0)
range = minimum range to first pixel (has to be left) (default 7000.0)
psin = range pixel spacing of input data (default 3.0)
psout = desired range pixel spacing of output (default 3.0)